## Slide 1
Name | SRN
Parth Jadhav | 02fe23bec083
Md Danish Shamsher | 02fe23bec112
Roopashree | 02fe23bec122
Department of Electronics and Communication Engineering
RFID-Based Authorized Motor Control Using Raspberry Pi Pico H
Under the Guidance of
Dr. Vijay Rayar
Designation: Professor

## Slide 2
RFID-Based Authorized Motor Control
Using Raspberry Pi Pico H
A Secure Embedded System for Access-Controlled Motor Operation
RC522 RFID Module
L298N Motor Driver
Arduino IDE (C++)
Electronics & Communication Engineering | Mini Project Presentation

## Slide 3
INTRODUCTION
What is This Project?
🔐 RFID Authentication
RC522 module reads UID from NFC tags. Only a pre-programmed authorized UID starts the motor.
⚙️ Motor Control
L298N driver powers the DC motor at 12V. Motor runs continuously until a manual stop switch is pressed.
💡 LED Indication
Onboard LED on GP25 gives visual feedback — ON for authorized access, OFF on stop or rejection.
🛡️ Security Logic
Any unauthorized RFID tag is immediately rejected. System remains in idle state ready for the next scan.
Raspberry Pi Pico H • RC522 RFID • L298N • Arduino IDE

## Slide 4
LITERATURE SURVEY
Related Work & Background
01
RFID in Access Control Systems
RFID technology has been widely adopted in physical access control since the 1990s. Studies show ISO/IEC 14443-A protocol (used by MFRC522) provides reliable 13.56 MHz NFC tag reading with UID uniqueness for authentication.
02
Embedded Motor Control via SPI
L298N H-bridge motor drivers are a standard choice for DC motor control in embedded systems. PWM-based speed control via ENA pin and direction via IN1/IN2 is well-documented in literature.
03
RP2040 vs ESP8266 for RFID
Unlike ESP8266-targeted RFID libraries, the RP2040 (Pico) works best with Arduino-compatible MFRC522 libraries. MicroPython alternatives suffer from platform compatibility issues as observed in this project.
04
Security in RFID-Based Systems
UID-based authentication is a practical first-level security measure. Literature recommends it for low-cost embedded prototypes where cryptographic RFID protocols are not required.

## Slide 5
PROBLEM STATEMENT & OBJECTIVES
What We Solved & Why
⚠ Problem Statement
Industrial machinery and motorized systems lack low-cost access control. Physical switches alone do not prevent unauthorized operation. A secure, embedded RFID-based system is needed to allow only authorized users to start a motor.
✅ Objectives
Implement UID-based RFID authentication on Raspberry Pi Pico H
Control a 12V DC motor via L298N based on access status
Provide visual LED feedback for authorized / denied access
Allow manual motor stop using a push button switch
2
RFID Tags
(1 Auth / 1 Denied)
12V
Motor Supply
voltage
SPI
Communication
Protocol
1
Stop Switch
(GP17)

## Slide 6
SYSTEM REQUIREMENTS & SPECIFICATIONS
Hardware & Software Specifications
Hardware
Component | Specification
Raspberry Pi Pico H | RP2040, 133MHz, 2MB Flash
RC522 RFID Module | 13.56 MHz, SPI, 3.3V
L298N Motor Driver | Dual H-bridge, 12V, 2A
DC Motor | 12V DC, 300 RPM
Stop Switch | Tactile Push Button, GPIO Pull-Up
Power Supply | 12V Adapter → L298N; 5V USB → Pico
Software & Pin Mapping
Item | Detail
IDE | Arduino IDE 2.x
Board Package | earlephilhower RP2040
RFID Library | MFRC522 by GithubCommunity
SDA / CS | GP5
SCK / MOSI / MISO | GP2 / GP3 / GP4
RST / ENA / IN1 / IN2 | GP6 / GP14 / GP15 / GP16
Authorized UID: 99 142 40 3 | Unauthorized UID: 2 232 199 1

## Slide 7
TOOLS USED
Development Tools & Components
Arduino IDE 2.x
Software
Primary development environment. Chosen over Thonny/MicroPython due to stable MFRC522 library support for RP2040.
MFRC522 Library
Library
By GithubCommunity. Handles SPI communication, tag detection, and UID extraction from RC522 module.
RP2040 Board Pkg
Board Support
earlephilhower/arduino-pico. Adds Raspberry Pi Pico H support to Arduino IDE with full SPI peripheral access.
RC522 Module
Hardware
13.56 MHz RFID reader. Communicates via SPI. Version register = 0x92 confirmed wiring during debugging.
L298N Driver
Hardware
H-bridge IC for bidirectional DC motor control. ENA (PWM), IN1, IN2 control speed and direction from GP14–GP16.
Raspberry Pi Pico H
Microcontroller
RP2040 dual-core ARM Cortex-M0+. 133 MHz, SPI0/SPI1 peripherals used for RC522. Pre-soldered headers (H variant).

## Slide 8
SYSTEM ARCHITECTURE & BLOCK DIAGRAM
How the System is Connected
12V Supply
Adapter
L298N
Motor Driver
DC Motor
12V / OUT1-OUT2
Raspberry Pi Pico H
RP2040 | GP2–GP17
ENA/IN1/IN2
RC522
RFID Module (SPI)
SPI (GP2–GP6)
Auth Tag
Denied Tag
Stop Switch
GP17 Pull-Up
Signal
Onboard LED
GP25
PWM/DIR
Common GND: Pico GND ←→ L298N GND | RC522 VCC → Pico 3.3V | L298N 12V → Adapter +

## Slide 9
MODEL-BASED DESIGN
Finite State Machine Design
IDLE
Waiting for
RFID Scan
AUTH
UID Check
(Match?)
RUNNING
LED ON
Motor ON
DENIED
LED OFF
Motor OFF
Tag Scanned
Authorized ✓
Denied ✗
Stop Button →
Back to IDLE
Auto Reset
IDLE State
Auth Check
Motor Running
Access Denied

## Slide 10
SIMULATION & ANALYSIS
Platform Debugging & Decision Analysis
01
Phase 1
FAILED
MicroPython Attempt
Thonny IDE used with existing MFRC522 lib. Correct init syntax MFRC522(spi, rst, cs) not supported. Library built for ESP8266 → RuntimeError: Unsupported platform on RP2040.
02
Phase 2
SUCCESS
SPI Debug Verification
Manually read Version Register via raw SPI. Got 0x92 → confirmed RC522 is working, SPI wiring correct, and power supply is adequate. Problem isolated to library.
03
Phase 3
SUCCESS
Switch to Arduino IDE
Installed earlephilhower/arduino-pico board package and MFRC522 by GithubCommunity. Both UIDs read correctly: 99 142 40 3 and 2 232 199 1.
04
Phase 4
SUCCESS
Full System Integration
Motor, LED, stop switch integrated with RFID logic. Authorized tag starts motor, unauthorized denied, stop button halts operation. All features working.

## Slide 11
HARDWARE IMPLEMENTATION
Circuit Connections & Code Structure
Pin Mapping Summary
GP2
RC522 SCK
GP3
RC522 MOSI
GP4
RC522 MISO
GP5
RC522 SDA (CS)
GP6
RC522 RST
GP14
L298N ENA (PWM)
GP15
L298N IN1
GP16
L298N IN2
GP17
Stop Switch
GP25
Onboard LED
Core Logic (Arduino / C++)
byte authUID[] = {99, 142, 40, 3};
void loop() {
if (!mfrc522.PICC_IsNewCardPresent())
return;
mfrc522.PICC_ReadCardSerial();
if (matchUID(mfrc522.uid.uidByte)) {
digitalWrite(LED, HIGH);
analogWrite(ENA, 200); // Motor ON
while (digitalRead(STOP) == HIGH);
stopMotor();
} else {
Serial.println("Access Denied");
}
}
Power: 12V Adapter → L298N 12V & GND | USB 5V → Pico | Common GND between Pico and L298N required

## Slide 12
TESTING & RESULTS
Test Cases & Observations
TC-01: Authorized Tag Scan
PASS
UID: 99 142 40 3
Input: Scan authorized NFC tag
Expected: Motor ON, LED ON
Serial: Access Granted
Motor Running
TC-02: Unauthorized Tag Scan
PASS
UID: 2 232 199 1
Input: Scan unauthorized NFC tag
Expected: Motor OFF, LED OFF
Serial: Access Denied
TC-03: Stop Switch Press
PASS
UID: —
Input: Press stop switch during run
Expected: Motor stops, LED OFF
Serial: Motor Stopped
TC-04: Re-scan After Stop
PASS
UID: 99 142 40 3
Input: Scan authorized tag again
Expected: Motor restarts
Serial: Access Granted
Motor Running

## Slide 13
APPLICATIONS & FUTURE SCOPE
Where This Goes Next
Current Applications
🏭 Industrial machine access control
🚗 Authorized vehicle ignition systems
🏗️ Conveyor belt access security
🔒 Server room / lab equipment lock
🏠 Smart home door/gate motor lock
Future Enhancements
🔐 AES-encrypted RFID (MIFARE auth)
📱 BLE / WiFi remote override via app
📊 Access log stored on SD Card
🔔 Buzzer alert for unauthorized scan
👥 Multi-user UID whitelist support
✅ Successfully built a fully working RFID-secured motor control system using Raspberry Pi Pico H and Arduino IDE — demonstrating embedded security, SPI communication, and motor driver integration in a compact hardware prototype.